The Discrete Fourier Transform
Spectral-based
Sound Transformations
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
http://mtg.upf.edu

---
Index
- Filtering
- Morphing
- Frequency scaling
- Time stretching

---
STFT implementation diagram
Short-time Fourier transform
w[n]
|X[k]|
x[n]
yw[n]
y[n]
FFT
IFFT
Overlap-add
xw[n]
<X[k]

---
STFT
[Speaker Notes: We were asked for an]

---
Filtering: Equalization

---
Morphing with STFT
[Speaker Notes: We were asked for an]

---
Morphing

---
Harmonic plus residual model
wh[n]
|X[k]|
x[n]
pr
fr
Ar
F0
detection
Peak detection
FFT
X
xwh[n]
ph
<X[k]
f0
fh
Ah
Sine spectral
synthesis
wr[n]
X[k]
-
Yh[k]
FFT
X
+
xwr[n]
Yr[k]
+
Y[k]
IFFT
yw[n]
Overlap-add
y[n]

---
Filtering sine waves
Filter=[ 0 2099 2100 3000 3001 fs/2; % Hz
-200 -200 0 0 -200 -200 ]; % db
ysmag = ysmag+interp1(Filter(1,:),Filter(2,:),ysloc/Ns*fs);

---
Frequency shifting of sine waves
fshift = 100;
ysloc = (ysloc>0).*(ysloc + fshift/fs*Ns);

---
Frequency stretching of sine waves
fstretch = 1.1;
ysloc = ysloc .* (fstretch.^[0:length(ysloc)-1]');

---
Pitch transposition with timbre preservation

---
Harmonic plus Stochastic model
wh[n]
|X[k]|
x[n]
pr
fr
Ar
F0
detection
Peak detection
FFT
X
xwh[n]
ph
<X[k]
f0
fh
Ah
Sine spectral
synthesis
wr[n]
-
X[k]
Yh[k]
FFT
X
+
Yr[k]
xwr[n]
Stochastic approximation
|Ys[k]|
<Ys[k]
Ys[k]
Random phase generation
Stochastic spec. synthesis
+
Y[k]
IFFT
yw[n]
Overlap-add
y[n]

---
Time scaling
It’s a frame based frequency domain technique
Windowing
&
Overlapp
Time
Scale
IFFT
FFT
input
output
AFn
SFm
AFn = Analysis Frame number n
SFm = Analysis Frame number m
Analysis and synthesis processes must use the same window size and window type
[Speaker Notes: This leaves time as the only degree of freedom and the only thing of interest then is to place the start and end points of each phoneme to be aligned. The most commonly used and also successful way to align voice to text is]

---
Frame positions
Used twice!
Analysis frames
TS>1
Synthesis frames
Not used!
Analysis frames
TS<1
Synthesis frames

---
The Time-Scale module
Phase
Spectrum Phase Generation
Z-1
Phase
AFn
Peak
Detection
Z-1
SFm
Peak
Continuation
Peak
Detection
Amplitude
Amplitude
[Speaker Notes: -Dynamic: The spectral characteristics of a voiced sound change with the loudness.]

---
Delta phase around each peak
The phase around each peak is obtained applying the delta phase function of the original frame
Amplitude
Amplitude
f1
f1
f2
f2
Phase
Phase
AFn
SFm
[Speaker Notes: -Vibrato: Two types of vibrato exist in singing. The classical vibrato in opera music corresponds to periodic modulation of the phonation frequency, and in popular music the vibrato implies an added amplitude modulation of the voice source. In speech, no vibrato exists.]

---
References
- http://en.wikipedia.org/wiki/Sound_effects
- http://en.wikipedia.org/wiki/Equalization_filter
- http://en.wikipedia.org/wiki/Audio_timescale-pitch_modification

---
Credits
All the slides of this presentation are released under an Attribution-Noncommercial-Share Alike license.