Introduction to Audio Signal Processing for Music Applications
[text for Intro-DSP.odp]

Welcome everyone!!

1.
In this first class of the Audio Signal Processing for Music Applications course I give an overview of what we understand for audio signal processing and I give a broad context to the more specific topics that we will cover in the course.

2.
I first define audio signal processing and then go over the most common applications of interest to music. Applications that use signal processing techniques, such as storage, level compression, data compression, enhancement, effects and transformations, synthesis, and sound description.

3.
We can define audio signal processing as the engineering field that focuses on the computational methods for intentionally altering sounds.

An audio signal processing system takes a sound, or a signal related to a sound, as input, and using some control parameters produces and output sound or any type of derived signal.

Since audio signals may be electronically represented in either digital or analog format, signal processing may occur in either domain. Analog processors operate directly on the electrical signal, while digital processors operate mathematically on the binary representation of that signal.

In this course we will focus on digital signals and systems.

4.
An analog sound is usually electrical; a voltage level represents the air pressure waveform of the sound. Thus it is a continuous function, like in this top plot.

A digital representation expresses the pressure waveform as binary numbers, thus it is a discrete function, like this bottom plot.

The digital representation permits signal processing using microprocessors and computers. Although the conversion from analog to digital can be prone to loss, most modern audio systems use this approach as the techniques of digital signal processing are much more powerful and efficient than analog domain signal processing.

5.
One application of signal processing techniques is the storage of sounds, thus their recording and reproduction.

Sound waves, such as spoken voice, environmental sounds or music can be recorded as electrical or mechanical inscriptions in a media and can then be recreated from these inscriptions.

These processes can be done using analog or digital technologies. But this is a topic that is not so relevant for our course and I will not say anything else.

6.
Another common application is dynamic level compression.

This is a process that reduces the dynamic range of an audio signal, that is, it narrows the difference between high and low audio levels or volumes, like it can be seen in these plots.

Level compression is commonly used during sound recording, live sound reinforcement, and broadcasting.

7.
Another signal processing application is data compression, or also called audio coding.

The goal here is to reduce the bandwidth requirement of digital audio streams and the storage size of audio files.

There are two types of compression techniques, the ones called lossless, which do not lose any information, and the ones called lossy, in which some information is lost, but hopefully this information lost is not perceptually relevant.

For example the .wav file format is based on a non compressed representation of a digital sound and the .mp3 format is a compressed representation that can be obtained from a .wav file using a perceptual based lossy technique. We will not cover this application in this course.

8.
Another set of applications relate to sound enhancement, which is a process that aims to improve the quality of a sound.

Such quality improvements can be done by filtering, equalizing, canceling the noise background, or removing echo or reverberation. Again this is a topic that we will not cover in this course.

9.
Another set of applications relate to performing sound transformations for more creative usages.

We can filtering techniques to add echo or reverb to a sound but there are many more sophisticated techniques with which we can change most of the characteristics of a sound, making it completely different.

We can use time domain techniques to create unusual sounds, using methods such as flangers, phasers, and chorus. We can change the pitch of a sound or modify the speed of an audio signal without affecting its pitch. We can morph the sound with another. We can perform 3D audio effects with which we can place sounds outside the stereo basis. The possibilities are huge.

In this course this will be one of the major applications that we will target.

10.
Another set of applications relate to sound synthesis, thus applying signal processing techniques with the aim to generate sounds, either imitating existing sounds or creating new timbres.

Many techniques have been developed for this purpose. Among the most common ones we can mention Additive synthesis, Subtractive synthesis, Granular synthesis, Physical modeling,
Frequency Modulation, and Waveshaping.

This course will not focus on synthesis but we will need to understand and use some of these techniques, specially additive synthesis and subtractive synthesis.

11.
The last group of applications I will mention are related to sound description, thus techniques that aim to analyze and describe a sound signal with the goal to describe and model meaningful characteristics of the sound.

This is a research field that has expanded enormously in the last few years and that is very relevant in sound and music search and retrieval applications.

We can talk about low-level audio features that can be extracted from a sound using signal processing techniques, related to sound characteristics like loudness, timbre and pitch.

We can also extract more musically relevant features related to musical concepts like rhythm, harmony and melody. We normally refer to this type of features as mid-level.

Following this progression we can also talk about high-level characteristics of a music signal in order to refer to aspects like genre, emotions, or about the music similarity between two signals. This normally cannot be accomplished with just signal processing techniques, we need to incorporate methodologies coming from fields such as machine learning or semantic analysis.

This aspect of sound description will also be an important one for this course. We will not be able to go over mid and high level features of a signal, but the discussions that we will have on the analysis of low level features are the first in the general topic of sound and music description.

12.
I want to finish by mentioning that all the material I will use and produce in this class is available under open licenses.

Most of the text references I used come from Wikipedia. The images that I have not generate myself will mostly come from http://commons.wikimedia.org/. All the sounds will come from http://freesound.org.

I will be using some free software applications to show examples, like Audacity in today's class.

All the slides, texts, videos, sounds, etc. that I have created for the course are released under a Creative Commons license, the Attribution-Noncommercial-Share Alike license.

All the software that we have written and that will be used for the labs, are based in Python and are released under Affero GPL license and is available from https://github.com/MTG/sms-tools

---------------

This is all for this first class. We have done a quick overview of the field of audio signal processing, too bad that we will not be able to cover everything. From now on we will focus on several core signal processings methodologies and we will exemplify them within a few music application areas.

I hope I have been able to interest you in following the course. Thanks for you attention!!