Some basic mathematics
Sinusoidal Modeling
(1 of 2)
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
http://mtg.upf.edu

---
Index
- Sinusoidal model
- Sinewave spectrum
- Sinusoidal detection
  - Peak detection
  - Peak interpolation

---
Sinusoidal model
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n)} newline newline alignl {R: "number of sinewave components"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency"} newline

---
Sinewave spectrum
alignl{x[n] = A cos(2%pi k_0 n/N + %phi)} newline alignl{X[k]= A sum from{n=0} to{N-1} w[n] 1 over 2 {(e^{j 2%pi k_0 n/N} + e^{-j 2%pi k_0 n/N})} e^{-j 2%pi kn/N}}newline alignl{~~~~~ = A over 2 sum from{n=0} to{N-1} w[n] e^{j 2%pi k_0 n/N} e^{-j 2%pi kn/N} + A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi k_0 n/N} e^{-j 2%pi kn/N}}newline alignl{~~~~~ = A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi ( - k_0 + k)n/N} + A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi (k_0 + k)n/N}}newline alignl{~~~~~ = A over 2 W[-k_0+k] + A over 2 W[k_0+k]}

---
Sinewave spectrum

---
Sinusoidal detection – freq. resolution

---
Peak detection
- A peak is defined as a local maximum in the magnitude spectrum.
- Each peak location is accurate only to within half a sample.
- Zero-padding increases the number of DFT samples (bins) per Hz and thus increases the accuracy of peak detection.
- A better peak detection strategy is based on combining zero-padding with some spectral interpolation.

---
Peak detection and window-size
To resolve two sinusoids separated in frequency by ∆Hz we require main-lobe bandwidth Bf <= ∆
and
If
where main-lobe bandwidth in bins, sampling rate,
M: window length, and frequencies of the sinusoids.
If and are successive harmonics of a fundamental frequency ,
Then . Harmonic resolution requires and
Since the period in samples is , then
size 24{M geslant B_s f_s / f_1}
size 24{M geslant B_s P}

---
Peak phase

---
Peak detection

---
Peak detection with zero-padding

---
Parabola
p: center of the parabola
a: measure of concavity
b: offset

---
Peak interpolation
%beta
o
%gamma
o
%alpha
o
-1
+1
0
Center of the parabola:
hat{k}_p = hat{k} + {{%alpha - %gamma} over 2} (%alpha - 2%beta + %gamma)
hat{a} = %beta - {hat{k}_p over 4} (%alpha - %gamma)
Amplitude:

---
Peak detection with interpolation

---
Sinusoidal parameters from peaks
alignl{{hat{k}_p} = lline X[k_p] rline + {0.5 * (lline X[k_p-1]rline -lline X[k_p+1]rline)}over {lline X[k_p-1]rline -2*lline X[k_p]rline + lline X[k_p+1] rline}}newline newline newline alignl{f_p = f_s * {hat{k_p} over N}}newline newline alignl{A_p = lline X[k_p]rline - 0.25 * (lline X[k_p - 1]rline - lline X[k_p+1]rline)*(hat{k_p} - k_p)} newline newline alignl{ph_p = %angle X[hat{k_p}]} newline newline

---
References
- https://ccrma.stanford.edu/~jos/sasp/Spectrum_Analysis_Sinusoids.html
- http://en.wikipedia.org/wiki/Additive_synthesis

---
Credits
All the slides of this presentation are released under an Attribution-Noncommercial-Share Alike license.