The Discrete Fourier Transform
Sinusoidal plus Residual Modeling
(1 of 2)
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
http://mtg.upf.edu

---
Index
- Sinusoidal plus residual model
- Sinusoidal subtraction
- Stochastic model

---
Sinusoidal plus residual model
Sinusoidal plus residual model
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n) + yr[n] = ys[n] + yr[n]} newline alignl {R: "number of sinusoidal components"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency"} newline alignl {yr[n]: "residual component"} newline alignl {ys[n]: "sinusoidal component"} newline
when yr[n] is an stochastic signal, it can be modeled as filtered white noise:
alignl{yr_l[n] =yst_l[n] = sum from {k=0} to {N-1} u[n] h_l[n-k]} newline alignl{u[n]: "white noise"}newline alignl{h[n]: "impulse response of filter approximating residual component"}newline alignl{l: "frame number"}newline
alignl {yr[n] = x[n] - sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n)} = x[n] - ys[n]
otherwise:

---
Spectral view of SpR model
alignl {Y_l[k] = sum from {r=1} to {R_l} A_{(r,l)} W[k-{hat f}_{(r,l)}] + Yr_l[k] = Ys_l[k] + Yr_l[k] } newline alignl {W: "spectrum of analysis window"} newline alignl {R_l: "number of sinusoidal components"} newline alignl {A_{(r,l)}: "Amplitude of sinusoid"} newline alignl {{hat f}_{(r,l)}: "Normalized frequency of sinusoid"} newline alignl {Yr_l: "residual component spectrum"} newline alignl {Ys_l: "sinusoidal component spectrum"} newline alignl {l: "frame number"} newline
when e[n] is an stochastic signal, it can be modeled as filtered white noise:
alignl{Yr_l[k] = Yst_l[k] = U[k]H_l[k]} newline alignl{U: "white noise spectrum"}newline alignl{H_l: "frequency response of filter apporximating residual component"}newline
otherwise:
alignl {Yr_l[k] = X_l[k] - Ys_l[k]}

---
Residual modeling
Stochastic signals
- Stochastic processes
  - described by the laws of probability, mean, variance, probability distributions
- Autocorrelation
- Power spectral density
alignl{Z_{xx}[k] = sum from {n=0} to {n=N-1} x[n] x[n+k]~~~k=-N+1,...,N-1}
alignl{Xp [k] = lim csub {N rightarrow infinity} {abs{X[k]}}^2} newline alignl{"where "X[k] = sum from{n=0} to{N-1} {x[n] e^{-j 2%pi kn/N}}~~k=0,..., N-1} newline

---
Stochastic model
alignl{yst[n] = sum from {k=0} to {N-1} u[n] h[n-k]} newline newline alignl{u[n]: "white noise"}newline alignl{h[n]: "impulse response of filter approximating input signal" x[n]}newline
Spectral view:
alignl{Yst_l[k] = {lline {H}_l[k] rline} {lline {U}[k] rline} e^({%angle H[k]}+{%angle U[k]}) = {lline {tilde X}_l[k] rline} e^{%angle U[k]} } newline newline alignl{{lline{tilde X}[k] rline}: "approximation of magnitude spectrum of input signal" x[n]}newline alignl{%angle U[k]: "spectral phases of noise signal"}newline alignl{l: "frame number"}newline

---
References
- https://ccrma.stanford.edu/~jos/sasp/Spectrum_Analysis_Sinusoids.html
- http://en.wikipedia.org/wiki/Stochastic_process
- http://en.wikipedia.org/wiki/Linear_predictive_coding
- Sounds: http://www.freesound.org/people/xserra/packs/13038/

---
Credits
All the slides of this presentation are released under an Attribution-Noncommercial-Share Alike license.