The Discrete Fourier Transform
Harmonic Model
Xavier Serra
Universitat Pompeu Fabra, Barcelona
[Speaker Notes: If you are watching this it hopefully means that you have followed the course on Audio Signal Processing for Music Applications until here. You just reached the half point, congratulations!!! In the last lectures we talked about the sinusoidal model. In order to continue with the idea of having more flexible and higher level representations of sounds in this lecture we present the harmonic model.]

---
Index
- Harmonic model
- Sinusoids-partials-harmonics
- Monophonic-polyphonic signals
- Harmonic detection (after F0 detection)
- Harmonic model system

---
Harmonic model
alignl {yh[n] = sum from {r=1} to R A_r[n] cos (2 %pi rf_0[n]n)} newline newline alignl {R: "number of harmonic components"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_0[n]: "fundamental frequency (Hz)"} newline

---
Spectral view
alignl {Yh_l[k] = sum from {r=1} to {R_l} A_{(r,l)} W[k-r{hat f}_{(0,l)}]} newline newline alignl {W[k]: "spectrum of analysis window"} newline alignl {R_l: "number of harmonics"} newline alignl {A_{(r,l)}: "amplitude of harmonics"} newline alignl {{hat f}_{(0,l)}: "normalized fundamental frequency"} newline alignl {l: "frame number"} newline

---
Sinusoids-Partials-Harmonics

---
Sinusoids-Partials-Harmonics

---
Monophonic-Polyphonic signals

---
Harmonic detection
Harmonic stable peak whose frequency is close to a multiple of the fundamental frequency.
alignl{"Condition for a peak" f_p "of frame" l }newline alignl{"to be part of a harmonic frequency" f_h:}newline newline alignl{f_p[l] = f_h[l] ~"if"~ (lline f_p[l] -(h*f_0[l]) rline~ < ~ threshold)}newline alignl{ ~~~~~~"and exists" ~ f_h[l-2], f_h[l-3],... ,f_h[l-L] }

---
Implementation: Harmonic Model
Harmonic model system
w[n]
f0
|X[k]|
pp
fp
Ap
x[n]
Harmonic
detection
F0
detection
Peak detection
FFT
X
xw[n]
<X[k]
ph
fh
Ah
Analysis
Synthesis
Sine spectral
synthesis
Yh[k]
IFFT
yhw[n]
Overlap-add
yh[n]

---
References and credits
- More information on this topic from Wikipedia:
  - https://en.wikipedia.org/wiki/Harmonic_series_(music)
  - https://en.wikipedia.org/wiki/Harmonic
- Sounds used taken from Freesound: http://www.freesound.org/people/xserra/packs/13038/
- All slides and code produced for this course are released using the CC Attribution-Noncommercial-Share Alike license or the Affero GPL license and available from https://github.com/MTG/sms-tools