Some basic mathematics
The Short-Time Fourier Transform
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
http://mtg.upf.edu

---
Index
- Short-time Fourier Transform equation
- Window type
- Window size
- FFT size
- Hop size
- Time-frequency compromise
- Inverse STFT
- STFT implementation

---
Introduction: STFT
Short-time Fourier Transform
X_l[k] = sum from{n=-N/2} to{N/2-1} w[n]{x[n+lH] e^{-j 2%pi kn/N}}~~l=0,1,...,
w: real window
l: number of frame
H: time advance of window (hop-size)

---
w[n]x[n+lH] ~~~~l=0,1,...,

---
Transform of a windowed sinewave
alignl {x[n]= A_0 cos (2%pi k_0 n/N) = {A_0} over {2} e^{j2%pi k_0 n /N}+ {A_0} over {2} e^{-j2%pi k_0 n/N}}
alignl{X[k] = sum from{n=-N/2} to{N/2-1} {w[n] x[n] e^{-j 2%pi kn/N}}} newline alignl{~~~~~= sum from{n=-N/2} to{N/2-1}w[n] ({A_0} over {2} e^{j2%pi k_0 n / N}+ {A_0} over {2} e^{-j2%pi k_0 n/N}) {e^{-j 2%pi kn/N}}}newline alignl{~~~~~= sum from{n=-N/2} to{N/2-1}{w[n]{A_0} over {2}} e^{j2%pi k_0 n / N} {e^{-j 2%pi kn/N}} + sum from{n=-N/2} to{N/2-1} {w[n]{A_0} over {2}} e^{-j2%pi k_0 n/N} {e^{-j 2%pi kn/N}}}newline alignl{~~~~~= {{A_0} over {2}} sum from{n=-N/2} to{N/2-1}w[n] e^{-j2%pi (k-k_0) n / N} + {{A_0} over {2}} sum from{n=-N/2} to{N/2-1} w[n] e^{-j2%pi (k+k_0) n/N}}newline alignl{~~~~~= {{A_0} over {2}} W[k-k_0] + {{A_0} over {2}} W[k+k_0]}

---
N = 256
M = 63
f0 = 1000
fs = 10000
A0 = .8
hN = N/2
hM = (M+1)/2
x = A0 * np.cos(2*np.pi*f0/fs*np.arange(-hM+1,hM))
w = np.hanning(M)
plt.subplot(2,3,1)
plt.plot(np.arange(-hM+1, hM), w, 'b')
fftbuffer[:hM] = w[hM-1:]
fftbuffer[N-hM+1:] = w[:hM-1]
X = fft(fftbuffer)
X1[:hN] = X[hN:]
X1[N-hN:] = X[:hN]
mX = 20*np.log10(abs(X1))
plt.subplot(2,3,2)
plt.plot(np.arange(-hN, hN), mX, 'r')
pX = np.angle(X1)
plt.subplot(2,3,3)
plt.plot(np.arange(-hN, hN), np.unwrap(pX), 'g')
plt.subplot(2,3,4)
xw = x*w
plt.plot(np.arange(-hM+1, hM), xw, 'b')
fftbuffer[0:hM] = xw[hM-1:]
fftbuffer[N-hM+1:] = xw[:hM-1]
X = fft(fftbuffer)
X2[:hN] = X[hN:]
X2[N-hN:] = X[:hN]
mX2 = 20*np.log10(abs(X2))
plt.subplot(2,3,5)
plt.plot(np.arange(-hN, hN), mX2, 'r')
pX = np.angle(X2)
plt.subplot(2,3,6)
plt.plot(np.arange(-hN, hN), np.unwrap(pX), 'g')

---
Window type
All standard windows are real and symmetric and have a frequency spectrum with a sinc-like shape.
rectangular
window
magnitude
spectrum
The choice is mainly determined by two of the spectrum’s characteristics:
 1. Width of main lobe
 2. Highest side-lobe level

---
Window functions
Window functions in Scipy
barthann (M[, sym])	Return a modified Bartlett-Hann window.
bartlett (M[, sym])	Return a Bartlett window.
blackman (M[, sym])	Return a Blackman window.
blackmanharris (M[, sym])	Return a minimum 4-term Blackman-Harris window.
bohman (M[, sym])	Return a Bohman window.
boxcar (M[, sym])	Return a boxcar or rectangular window.
chebwin (M, at[, sym])	Return a Dolph-Chebyshev window.
flattop (M[, sym])	Return a flat top window.
gaussian (M, std[, sym])	Return a Gaussian window.
general-gaussian (M, p, sig[, sym])	Return a window with a generalized Gaussian shape.
hamming (M[, sym])	Return a Hamming window.
hann (M[, sym])	Return a Hann window.
kaiser (M, beta[, sym])	Return a Kaiser window.
nuttall (M[, sym])	Return a minimum 4-term Blackman-Harris window according to Nuttall.
parzen (M[, sym])	Return a Parzen window.
slepian (M, width[, sym])	Return a digital Slepian window.
triang (M[, sym])	Return a triangular window.

---
Rectangular window
elsewhere
main-lobe width: 2 bins
side-lobe level: -13.3 dB

---
import matplotlib.pyplot as plt
import numpy as np
from scipy.fftpack import fft
M = 64
N = 1024
hN = N/2
hM = M/2
fftbuffer = np.zeros(N)
fftbuffer[hN-hM:hN+hM]=np.ones(M)
plt.subplot(2,1,1)
plt.plot(np.arange(-hN, hN), fftbuffer, 'b')
X = fft(fftbuffer)
mX = 20*np.log10(abs(X))
mX1[:hN] = mX[hN:]
mX1[N-hN:] = mX[:hN]
plt.subplot(2,1,2)
plt.plot(np.arange(-hN, hN), mX1-max(mX), 'r')

---
Hanning window
where
main-lobe width: 4 bins
side-lobe level: -31.5 dB

---
Hamming window
main-lobe width: 4 bins
side-lobe level: -42.7 dB

---
Blackman window
w[n] = 0.42 - 0.5 cos(2%pi n / M) + 0.08 cos(4 %pi n/M)
main-lobe width: 6 bins
side-lobe level: -58 dB

---
Blackman-Harris window
minimum 4-term Blackman-Harris window
alignl{w(n) = {1 over M} sum from {l=0} to {3} %alpha_l cos(2 n l %pi / M), ~n= -M/2, ...0, ... M/2} newline alignl{"where" ~ %alpha_0 = 0.35875, %alpha_1 = 0.48829, %alpha_2 = 0.14128, %alpha_3 = 0.01168}
alignl{ital{"main lobe width"} : 9"bins"} newline alignl{ital{"side-lobe level"} : -92dB}

---
Window size
Affects the time versus frequency resolution
M = 128
M = 1024

---
(fs, x) = read('oboe.wav')
N = 128
start = .8*fs
xw = x[start:start+N] * np.hamming(N)
plt.subplot(321)
plt.plot(np.arange(start, (start+N), 1.0)/fs, xw)
X = fft(xw)
mX = 20 * np.log10(abs(X)/N)
pX = np.unwrap(np.angle(X))
plt.subplot(323)
plt.plot(np.arange(0, fs/2.0, float(fs)/N), mX[0:N/2])
plt.subplot(325)
plt.plot(np.arange(0, fs/2.0, float(fs)/N), pX[:N/2])
N = 1024
start = .8*fs
xw = x[start:start+N] * np.hamming(N)
plt.subplot(322)
plt.plot(np.arange(start, (start+N), 1.0)/fs, xw)
X = fft(xw)
mX = 20 * np.log10(abs(X)/N)
pX = np.unwrap(np.angle(X))
plt.subplot(324)
plt.plot(np.arange(0, fs/2.0, float(fs)/N), mX[0:N/2])
plt.subplot(326)
plt.plot(np.arange(0, fs/2.0, float(fs)/N), pX[:N/2])

---
Even-Odd size Window

---
FFT size
FFT size, N, should be equal or larger than the window size, M
size 20 {M = 512}
size 20 {M = 512} newline size 20 {N=512}
size 20 {M = 512} newline size 20 {N=1024}

---
(fs, x) = read('oboe.wav')
M = 512
N = 512
start = .8*fs
xw = x[start:start+M] * np.hamming(M)
plt.subplot(311)
plt.plot(np.arange(start, (start+M), 1.0)/fs, xw)
X = fft(xw, N)
mX = 20 * np.log10(abs(X)/N)
pX = np.unwrap(np.angle(X))
plt.subplot(312)
plt.plot(np.arange(0, fs/2.0, float(fs)/N), mX[0:N/2])
M = 512
N = 1024
start = .8*fs
xw = x[start:start+M] * np.hamming(M)
X = fft(xw, N)
mX = 20 * np.log10(abs(X)/N)
plt.subplot(313)
plt.plot(np.arange(0, fs/2.0, float(fs)/N), mX[0:N/2])

---
Hop size
Successive frames should overlap in time in such a
way that all the data are weighted equally.
For certain windows exists perfect overlap factors.
Rectangular: M/j, Hanning and Hamming: (M/2)/j,
where j = 0, 1, ....
The overlap factor can be expressed by:
alignl{A_w[n] = sum from {l=0} to {L-1} w[n-lH] = c}

---
Time-frequency compromise
M=226
N=256
H=128
M=1024
N=1024
H=128

---
from pylab import *
from scipy.io.wavfile import read
(fs, x) = read('piano.wav')
subplot(2,1,1)
specgram(x, NFFT=256, Fs=fs, noverlap=128)
subplot(2,1,2)
specgram(x, NFFT=1024, Fs=fs, noverlap=128)

---
Inverse STFT
Inverse STFT
alignl{y[n] = sum from{l=0} to{L-1} Shift_{lH,n} {[{1 over N}{sum from{k=-N/2} to{N/2-1} X_l[k] e^{j 2%pi kn/N}}]}}
each synthesized frame is:
alignl{yw_l[n] = x(n+lH)w[n]}
and the synthesized sound is:
alignl{y[n] = sum from {l=0} to {L-1} yw_l[n] = x[n]sum from {l=0} to {L-1} w[n-lH]}

---
w[n]x[n+lH] ~~~~l=0,1,...,

---
STFT implementation diagram
STFT implementation diagram
w[n]
|X[k]|
x[n]
yw[n]
y[n]
FFT
IFFT
Overlap-add
xw[n]
<X[k]

---
def stft(x, fs, w, N, H):
  hN = N/2
  hM = (w.size+1)/2
  pin = hM
  pend = x.size-hM
  w = w / sum(w)
  while pin<pend:
  #-----analysis-----
    xw = x[pin-hM:pin+hM-1] * w
    fftbuffer[:hM] = xw[hM-1:]
    fftbuffer[N-hM+1:] = xw[:hM-1]
    X = fft(fftbuffer)
    mX = 20 * np.log10( abs(X[:hN]) )
    pX = np.unwrap( np.angle(X[:hN]) )
  #-----synthesis-----
    Y[:hN] = 10**(mX/20) * np.exp(1j*pX)
    Y[hN+1:] = 10**(mX[:0:-1]/20) * np.exp(-1j*pX[:0:-1])
    fftbuffer = np.real( ifft(Y) )
    yw[:hM-1] = fftbuffer[N-hM+1:]
    yw[hM-1:] = fftbuffer[:hM]
    y[pin-hM:pin+hM-1] += H*yw
    pin += H
  return y

---
References
- https://ccrma.stanford.edu/~jos/sasp/
- https://en.wikipedia.org/wiki/STFT
- https://en.wikipedia.org/wiki/Window_function
- Full code of plots and accompanying labs available at: https://github.com/MTG/sms-tools

---
Credits
All the slides of this presentation are released under an Attribution-Noncommercial-Share Alike license.