Some basic mathematics
Sinusoidal model
(1 of 2)
Xavier Serra
Universitat Pompeu Fabra, Barcelona
[Speaker Notes: Welcome again to the course on Audio Signal Processing for Music applications!! In the last lectures we talked about the Short-time Fourier Transform. That offered a great sound representation with which we can analyze and synthesize sounds without lossing any information, and at the same time it is a good tool for understanding, describing and transforming sounds. In this lecture we go a step further in the direction of obtaining a higher-level representation, that in exchange of losing a bit in terms of the identiy properties of the STFT we gain quite a lot of flexibility and level of abstraction in the representation. This is what we call the sinusoidal model.]

---
Index
- Sinusoidal model
- Spectrum of sinewave
- Sinewaves as spectral peaks
- Time-varying sinewaves in spectrogram
[Speaker Notes: In this first part of this lecture we will go over ...]

---
Sinusoidal model
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n)} newline newline alignl {R: "number of sinewaves"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency (Hz)"} newline
[Speaker Notes: The sine model is very simple, it is just a sum of time-varying sinusoids. ...]

---
Spectrum of sinewave
alignl{x[n] = A cos(2%pi k_0 n/N + %phi)} newline alignl{X[k]= A sum from{n=0} to{N-1} w[n] 1 over 2 {(e^{j 2%pi k_0 n/N} + e^{-j 2%pi k_0 n/N})} e^{-j 2%pi kn/N}}newline alignl{~~~~~ = A over 2 sum from{n=0} to{N-1} w[n] e^{j 2%pi k_0 n/N} e^{-j 2%pi kn/N} + A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi k_0 n/N} e^{-j 2%pi kn/N}}newline alignl{~~~~~ = A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi ( - k_0 + k)n/N} + A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi (k_0 + k)n/N}}newline alignl{~~~~~ = A over 2 W[k-k_0] + A over 2 W[k+k_0]}
[Speaker Notes: But we are interested in modeling the sinusoids in the frequency domain, in the spectrum. So let's see what that looks. ...]

---
[Speaker Notes: If we start from a sinewave ... the positive size of its spectrum will looks like this ...]

---
[Speaker Notes: Let's make it a bit more dificult, what happends when our sound includes two sinewaves. ...]

---
[Speaker Notes: and let's do an example from a real sound ...]

---
Sinewaves as spectral peaks
- Sinusoid peak in magnitude spectrum
- Frequency resolution: 1/2 bin
- Improvement of frequency resolution by:
  - zero-padding
  - spectral interpolation
[Speaker Notes: A simple way to identify the sinusoids in the spectrum is by just focusing on their peaks in the magnitude spectrum, thus with a location and height. The location is the frequency and the height is the amplitude of the sinusoid. ...]

---
Spectral peaks and window-size
{alignl {size 24{"If" B_f = B_s f_s / M ~ "and" ~ %iDELTA = lline f_{k+1} - f_k rline}}}
{alignl {size 20 {B_s="main-lobe bandwidth of window"}}}newline {alignl {size 20 {f_s="sampling rate in Hz"}}}newline {alignl {size 20 {M="window size"}}}newline {alignl {size 20 {f_k "and" f_{k+1}="frequency of sinusoids in Hz"}}}
{alignl{size 24 {M geslant B_s f_s over %iDELTA = B_s {alignc f_s} over {lline f_{k+1} - f_k rline}}}}
{alignl {size 20{"If" f_0 = %iDELTA, ~"then"~ B_f leslant f_0}}} newline {alignl {size 20{"and"~ M geslant B_s f_s / f_0, ~"or"~ M geslant B_s P,}}} newline {alignl {size 20 {"where"~ P = "period in samples"}}}
[Speaker Notes: To detect the spectral peaks we have to understand the effect of the window. The most important factor is the window size. ...]

---
{alignl {size 20{"Hamming window": B_s = 4}}} newline {alignl {size 20{f_s = 44100 "Hz"}}}newline {alignl {size 20{f_k = 440 "Hz"; f_{k+1} = 490 "Hz"}}}newline
{alignl{size 24 {M geslant B_s {alignc f_s} over {lline f_{k+1} - f_k rline} =4 {alignc 44100} over {lline 490 - 440 rline} = 3528}}}
[Speaker Notes: Let's put an example, ..]

---
[Speaker Notes: and let's see what happens with different sounds. ...]

---
[Speaker Notes: and let's look at a real sound ...]

---
Peak detection
alignl{size 20 {p_r = mX[k_0] ~"when"~ mX[k_0-1]<mX[k_0]>mX[k_0+1]}}newline alignl{size 18 {mX = "magnitude spectrum"; r = "peak number"; k_0 = "peak location"}}
[Speaker Notes: So if we choose the window size correctly we will have a peak for every sinusoid in the signal. Then to measure the frequency and amplitude of each sinusoid we have to just have to find the tip of the peak and its height. ... To find the phase of the sinusoid in the center of the window, we just get the phase of the point we detected in the magnitude. There is a little problem!!!, not enough resolution.]

---
Peak detection with zero-padding
[Speaker Notes: One solution for the resolution is to do zero-padding. To use an FFT size much larger than the window size. ... But if we want a good enough resolution we will need to increase the FFT size a lot, and that will be quite computationally expensive. any other solution?]

---
Parabola
p: center of parabola
a: concavity measure
b: offset
{size 24 {alignl{x[n] = a (n - p)^2 + b}}}
[Speaker Notes: We can do a cheeper interpolation by using. For example parabolic interpolation. The parabola is a function with a shape quite similar to the tip of the lobe of the spectrum of the analysis windows, in dB scale. ....]

---
Peak interpolation
%beta
o
%gamma
o
{alignl {size 24 {x[-1]~ = ~%ialpha~ = ~ mX[k_{%ibeta} -1]}}} newline {alignl {size 24 {x[0]~ = ~%ibeta~ = ~ mX[k_{%ibeta}]}}} newline {alignl {size 24 {x[1]~ = ~%igamma~ = ~ mX[k_{%ibeta} + 1]}}}
%alpha
o
-1
+1
0
Center of the parabola:
{hat k}_p = {hat k} + {{%alpha - %gamma} over 2} (%alpha - 2%beta + %gamma)
hat{a} = %beta - {hat k}_p over 4 (%alpha - %gamma)
Amplitude:
[Speaker Notes: To perform the parabolic interpolation on a spectral peak we can use the three highest values of the magnitude peak. ...]

---
Peak detection with interpolation
[Speaker Notes: Now iff we combine a bit of zero-padding and parabolic interpolation we get much better results. ... So this will give us a quite good measure of the frequency, amplitude, and phase of all the sinusoids present in a spectrum.]

---
Sinusoidal parameters from peaks
alignl{{hat k}_p} = lline X[k_p] rline + {0.5 * (lline X[k_p-1]rline -lline X[k_p+1]rline)}over {lline X[k_p-1]rline -2*lline X[k_p]rline + lline X[k_p+1] rline}newline newline newline alignl{f_p = f_s * {hat k}_p over {alignc N}}newline newline alignl{A_p = lline X[k_p]rline - 0.25 * (lline X[k_p - 1]rline - lline X[k_p+1]rline)*({hat k}_p - k_p)} newline newline alignl{ph_p = %angle X[{hat k}_p]} newline newline
[Speaker Notes: This is what we will get. ... But this is the values for a single frame and the sinusoidal models is about time-varying sounds, thus time-varying sinusoids.]

---
Sinewaves in spectrogram
- Sinusoid stable peak track in spectrogram
- Stability identified by
  - frequency and amplitude in succesive frames
  - phase derivative in time/freq
alignl{"Condition for a peak" f_p "of frame" l "to be part of a track" t:}newline newline alignl{f_p[l] = f_t[l]~ "if"~ (lline f_p[l] -f_t[l-1] rline ~< ~threshold)}newline alignl{ ~~~~~~"and if exists"~f_t[l-2], f_t[l-3],... ,f_t[l-L] }
[Speaker Notes: So we have to deal with spectrograms and find time-varying sinusoids there. ...]

---
[Speaker Notes: These are the sinusoidal tracks obtained from the sound of a bendir, a drum used in Turkey and other places. ...]

---
[Speaker Notes: If we plot the sinusoidal tracks on the phase spectrogram it is quite interesting. ...]

---
References and credits
- More information on this topic from Wikipedia:
  - http://en.wikipedia.org/wiki/Sinusoidal_model
- Reference for sinusoidal modeling by Julius O. Smith: https://ccrma.stanford.edu/~jos/sasp/Spectrum_Analysis_Sinusoids.html
- Sounds used taken from Freesound: http://www.freesound.org/people/xserra/packs/13038/
- Slides and code are released using the CC Attribution-Noncommercial-Share Alike license or the Affero GPL license and available from https://github.com/MTG/sms-tools
[Speaker Notes: On the topics covered until now there were many good references, but starting from this topic there is less. These techniques are more specific to in music applications and thus much less has been published. ...]

---
Sinusoidal model
(1 of 2)
Xavier Serra
Universitat Pompeu Fabra, Barcelona
[Speaker Notes: This is all for this class. We have presented the sinusoidal model, a sound representation built on top of the Short-time Fourier Transform that reduces the amount of information, geting rid of of non-relevant parts present in the spectrum. However its use to analyze sounds is not as easy as the STFT, we have to understand a bit about spectra and about windows in order to make good use of it. Hopefully you understood some of that in this lecture. Now we have to complete the explanation of the model by descriving the synthesis part. This is what we will do in the next lecture. Thanks for your attention.]