Some basic mathematics
The Short-Time Fourier Transform
(1 of 2)
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
http://mtg.upf.edu

---
Index
- Short-time Fourier Transform equation
- Window size
- FFT size
- Hop size
- Time-frequency compromise
- Inverse STFT
- STFT implementation

---
Introduction: STFT
Short-time Fourier Transform
X_l[k] = sum from{n=-N/2} to{N/2-1} w[n]{x[n+lH] e^{-j 2%pi kn/N}}~~l=0,1,...,
w: real window
l: number of frame
H: time advance of window (hop-size)

---
Window size
Affects the time versus frequency resolution
M = 128
M = 1024

---
(fs, x) = read('oboe.wav')
N = 128
start = .8*fs
xw = x[start:start+N] * np.hamming(N)
plt.plot(np.arange(start, (start+N), 1.0)/fs, xw)
X = fft(xw)
mX = 20 * np.log10(abs(X)/N)
pX = np.unwrap(np.angle(X))
plt.plot(np.arange(0, fs/2.0, float(fs)/N), mX[0:N/2])
plt.plot(np.arange(0, fs/2.0, float(fs)/N), pX[:N/2])
N = 1024
start = .8*fs
xw = x[start:start+N] * np.hamming(N)
plt.plot(np.arange(start, (start+N), 1.0)/fs, xw)
X = fft(xw)
mX = 20 * np.log10(abs(X)/N)
pX = np.unwrap(np.angle(X))
plt.plot(np.arange(0, fs/2.0, float(fs)/N), mX[0:N/2])
plt.plot(np.arange(0, fs/2.0, float(fs)/N), pX[:N/2])

---
Even-Odd size Window

---
FFT size
FFT size, N, should be equal or larger than the window size, M
size 20 {M = 512}
size 20 {M = 512} newline size 20 {N=512}
size 20 {M = 512} newline size 20 {N=1024}

---
(fs, x) = read('oboe.wav')
M = 512
N = 512
start = .8*fs
xw = x[start:start+M] * np.hamming(M)
plt.subplot(311)
plt.plot(np.arange(start, (start+M), 1.0)/fs, xw)
X = fft(xw, N)
mX = 20 * np.log10(abs(X)/N)
pX = np.unwrap(np.angle(X))
plt.subplot(312)
plt.plot(np.arange(0, fs/2.0, float(fs)/N), mX[0:N/2])
M = 512
N = 1024
start = .8*fs
xw = x[start:start+M] * np.hamming(M)
X = fft(xw, N)
mX = 20 * np.log10(abs(X)/N)
plt.subplot(313)
plt.plot(np.arange(0, fs/2.0, float(fs)/N), mX[0:N/2])

---
Hop size
Successive frames should overlap in time in such a
way that all the data are weighted equally.
For certain windows exists perfect overlap factors.
Rectangular: M/j, Hanning and Hamming: (M/2)/j,
where j = 0, 1, ....
The overlap factor can be expressed by:
alignl{A_w[n] = sum from {l=0} to {L-1} w[n-lH] = c}

---
N= 1000
M = 201
w = signal.blackman(M)
w1 = w/sum(w)
H = 100
pin = 0
pend = N - M
plt.subplot(211)
while pin<pend:
y [pin:pin+M] += w1*H
plt.plot(np.arange(pin, pin+M), w, 'b')
pin += H
plt.plot(np.arange(0, N), y, 'r')
H = 50
pin = 0
pend = N - M
plt.subplot(212)
while pin<pend:
y [pin:pin+M] += w1*H
plt.plot(np.arange(pin, pin+M), w, 'b')
pin += H
plt.plot(np.arange(0, N), y, 'r')

---
Time-frequency compromise

---
from pylab import *
from scipy.io.wavfile import read
(fs, x) = read('piano.wav')
subplot(2,1,1)
specgram(x,NFFT=256,window=hamming(256),Fs=fs,noverlap=128)
subplot(2,1,2)
specgram(x,NFFT=1024,window=hamming(1024),Fs=fs,noverlap=128)

---
Inverse STFT
Inverse STFT
alignl{y[n] = sum from{l=0} to{L-1} Shift_{lH,n} {[{1 over N}{sum from{k=-N/2} to{N/2-1} X_l[k] e^{j 2%pi kn/N}}]}}
each synthesized frame is:
alignl{yw_l[n] = x(n+lH)w[n]}
and the synthesized sound is:
alignl{y[n] = sum from {l=0} to {L-1} yw_l[n] = x[n]sum from {l=0} to {L-1} w[n-lH]}

---
yw_l[n]=w[n]y[n+lH] ~~~~l=0,1,...,

---
STFT implementation diagram
STFT implementation diagram
w[n]
|X[k]|
x[n]
yw[n]
y[n]
FFT
IFFT
Overlap-add
xw[n]
<X[k]

---
def stft(x, fs, w, N, H) :
  hN = N/2
  hM1 = int(math.floor((w.size+1)/2))
  hM2 = int(math.floor(w.size/2))
  pin = hM1
  pend = x.size-hM1
  w = w / sum(w)
  while pin<pend:
  #-----analysis-----
    xw = x[pin-hM1:pin+hM2]*w
    fftbuffer[:hM1] = xw[hM2:]
    fftbuffer[N-hM2:] = xw[:hM2]
    X = fft(fftbuffer)
    mX = 20 * np.log10( abs(X[:hN]) )
    pX = np.unwrap( np.angle(X[:hN]) )
  #----synthesis-----
    Y[:hN] = 10**(mX/20) * np.exp(1j*pX)
    Y[hN+1:]=10**(mX[:0:-1]/20)*np.exp(-1j*pX[:0:-1])
    fftbuffer = np.real( ifft(Y) )
    yw[:hM2] = fftbuffer[N-hM2:]
    yw[hM2:] = fftbuffer[:hM1]
    y[pin-hM1:pin+hM2] += H*yw
    pin += H
  return y

---
References
- https://ccrma.stanford.edu/~jos/sasp/
- https://en.wikipedia.org/wiki/STFT
- https://en.wikipedia.org/wiki/Window_function
- Full code of plots and accompanying labs available at: https://github.com/MTG/sms-tools

---
Credits
All the slides of this presentation are released under an Attribution-Noncommercial-Share Alike license.