The Discrete Fourier Transform
Sinusoidal plus Residual Modeling
(2 of 2)
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
http://mtg.upf.edu

---
Index
- Sinusoidal plus residual model
- Stochastic approximation of residual
- Sinusoidal plus stochastic model
- Harmonic plus Stochastic system diagram

---
Sinusoidal plus residual model
Sinusoidal plus residual model
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n) + yr[n] = ys[n] + yr[n]} newline alignl {R: "number of sinusoidal components"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency"} newline alignl {yr[n]: "residual component"} newline alignl {ys[n]: "sinusoidal component"} newline
when yr[n] is an stochastic signal, it can be modeled as filtered white noise:
alignl{yr_l[n] =yst_l[n] = sum from {k=0} to {N-1} u[n] h_l[n-k]} newline alignl{u[n]: "white noise"}newline alignl{h[n]: "impulse response of filter approximating residual component"}newline alignl{l: "frame number"}newline
alignl {yr[n] = x[n] - sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n)} = x[n] - ys[n]
otherwise:

---
Stochastic model
alignl{yst[n] = sum from {k=0} to {N-1} u[n] h[n-k]} newline newline alignl{u[n]: "white noise"}newline alignl{h[n]: "impulse response of filter approximating input signal" x[n]}newline
Spectral view:
alignl{Yst_l[k] = {lline {H}_l[k] rline} {lline {U}[k] rline} e^({%angle H[k]}+{%angle U[k]}) = {lline {tilde X}_l[k] rline} e^{%angle U[k]} } newline newline alignl{{lline{tilde X}[k] rline}: "approximation of magnitude spectrum of input signal" x[n]}newline alignl{%angle U[k]: "spectral phases of noise signal"}newline alignl{l: "frame number"}newline

---
IIR-filter approximation
Filter approximation
y[n] = sum from {k=1} to K a_k x[n-k] + A u[n]
LPC model:
{hat x}[n] = - sum from {k=1} to K a_k x[n-k]
e[n] =x[n] - {hat x}[n] = x[n] + sum from {k=1} to K a_k x[n-k]
E = sum from {n= - infinity} to {infinity} e[n]^2 = sum from {n= - infinity} to {infinity} (x[n] + sum from {k=1} to K a_k x[n-k])^2
The error is minimized by minimizing the mean of the total squared error with
respect to each of the parameters.

---
Residual synthesis
Stochastic synthesis using filters
Noise generation:
  - Algorithms for random number generation
  - White noise, other types of noises
  - Gaussian noise
direct form
structure
lattice
structure

---
Noise synthesis using IFFT
Stochastic synthesis using IFFT

---
Stochastic model of residual
Sinusoidal plus Stochastic model
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n) + yst[n]} newline alignl {R: "number of sinusoidal components"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency"} newline alignl {yst[n]: "stochastic signal"} newline
Spectral view:
alignl{Yst_l[k] = {lline {tilde Yr}_l[k] rline} e^{%angle U[k]} } newline newline alignl{{lline {tilde Yr}_l[k] rline}: "approximation of magnitude spectrum of input signal"}newline alignl{%angle U[k]: "spectral phases of noise"}newline alignl{l: "frame number"}newline

---
Implementation: Harmonic Model
Implementation: HpS model
wh[n]
|X[k]|
x[n]
pr
fr
Ar
F0
detection
Peak detection
FFT
X
xwh[n]
<X[k]
ph
f0
fh
Ah
Sine spectral
synthesis
wr[n]
-
X[k]
Yh[k]
FFT
X
+
Yr[k]
xwr[n]
Stochastic approximation
|Ys[k]|
<Ys[k]
Ys[k]
Random phase generation
Stochastic spec. synthesis
+
Y[k]
IFFT
yw[n]
Overlap-add
y[n]

---
References
- https://ccrma.stanford.edu/~jos/sasp/Spectrum_Analysis_Sinusoids.html
- http://en.wikipedia.org/wiki/Stochastic_process
- http://en.wikipedia.org/wiki/Linear_predictive_coding
- Sounds: http://www.freesound.org/people/xserra/packs/13038/

---
Credits
All the slides of this presentation are released under an Attribution-Noncommercial-Share Alike license.