Some basic mathematics
Sinusoidal Modeling
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
http://mtg.upf.edu

---
Index
- Sinusoidal model
- Sinewave spectrum
- Sinusoidal detection
  - Peak detection
  - Peak interpolation
- Sinusoidal synthesis
- Implementation

---
Sinusoidal model
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n)} newline newline alignl {R: "number of sinewave components"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency"} newline

---
Sinewave spectrum
alignl{x[n] = A cos(2%pi k_0 n/N + %phi)} newline alignl{X[k]= A sum from{n=0} to{N-1} w[n] 1 over 2 {(e^{j 2%pi k_0 n/N} + e^{-j 2%pi k_0 n/N})} e^{-j 2%pi kn/N}}newline alignl{~~~~~ = A over 2 sum from{n=0} to{N-1} w[n] e^{j 2%pi k_0 n/N} e^{-j 2%pi kn/N} + A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi k_0 n/N} e^{-j 2%pi kn/N}}newline alignl{~~~~~ = A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi ( - k_0 + k)n/N} + A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi (k_0 + k)n/N}}newline alignl{~~~~~ = A over 2 W[-k_0+k] + A over 2 W[k_0+k]}

---
Sinewave spectrum

---
Sinusoidal detection – freq. resolution

---
N = 1024
M1 = 221
M2 = 601
f0 = 1000
f1 = 1100
fs = 10000
A0 = .8
A1 = .5
hN = N/2
w1 = np.hanning(M1)
w2 = np.hanning(M2)
x = A0*np.cos(2*np.pi*f0/fs*np.arange(N))+
    A1*np.cos(2*np.pi*f1/fs*np.arange(N))
plt.subplot(3,1,1)
plt.plot(np.arange(N), x, 'b')
X = fft(x[0:M1]*w1, N)
mX = 20*np.log10(abs(X[0:hN]))
plt.subplot(3,1,2)
plt.plot((np.arange(hN)/float(N))*fs, mX-max(mX), 'r')
X = fft(x[0:M2]*w2, N)
mX = 20*np.log10(abs(X[0:hN]))
plt.subplot(3,1,3)
plt.plot((np.arange(hN)/float(N))*fs, mX-max(mX), 'r')

---
Peak detection
- A peak is defined as a local maximum in the magnitude spectrum.
- Each peak is accurate only to within half a sample.
- Zero-padding increases the number of DFT bins per Hz and thus increases the accuracy of peak detection.
- A better peak detection strategy is based on spectral interpolation.

---
Peak detection

---
Peak detection
def peak_detection(mX, hN, t):
  # mX: magnitude spectrum, hN: size of positive spectrum,
  # t: threshold
  thresh = np.where(mX[1:hN-1]>t, mX[1:hN-1], 0)
  next_minor = np.where(mX[1:hN-1]>mX[2:], mX[1:hN-1], 0)
  prev_minor = np.where(mX[1:hN-1]>mX[:hN-2], mX[1:hN-1], 0)
  ploc = thresh * next_minor * prev_minor
  ploc = ploc.nonzero()[0] + 1
  return ploc

---
Peak detection with zero-padding

---
Peak detection and window-size
To resolve two sinusoids separated in frequency by ∆Hz we require main-lobe bandwidth Bf <= ∆
and
If
where main-lobe bandwidth in bins, sampling rate,
M: window length, and frequencies of the sinusoids.
If and are successive harmonics of a fundamental frequency ,
Then . Harmonic resolution requires and
Since the period in samples is , then
size 24{M geslant B_s f_s / f_1}
size 24{M geslant B_s P}

---
N = 1024
hN = N/2
f0 = 400.0
fs = 10000.0
M = 6 * fs / f0
w = np.blackman(M)
x = signal.sawtooth(2 * np.pi * (f0/fs) * np.arange(M))
plt.figure(1)
plt.subplot(4,1,1)
plt.plot(np.arange(M)/fs, x, 'b')
plt.subplot(4,1,2)
plt.plot(np.arange(M), w, 'b')
xw = x * w
plt.subplot(4,1,3)
plt.plot(np.arange(M)/fs, xw, 'b')
X = fft(xw, N)
mX = 20*np.log10(abs(X[0:hN]))
plt.subplot(4,1,4)
plt.plot(fs*np.arange(hN)/N,mX-max(mX), 'r')

---
Peak phase

---
N = 1024
hN = N/2
M = 601
hM = (M+1)/2
w = np.blackman(M)
(fs, x) = wp.wavread('oboe.wav')
xw = x[40000:40000+M] * w
fftbuffer = np.zeros(N)
fftbuffer[:hM] = xw[hM-1:]
fftbuffer[N-hM+1:] = xw[:hM-1]
plt.subplot(3,1,1)
plt.plot(np.arange(N), fftbuffer, 'b')
X = fft(fftbuffer)
mX = 20*np.log10(abs(X[:hN]))
plt.subplot(3,1,2)
plt.plot(fs*np.arange(hN)/float(N),mX, 'r')
pX = np.unwrap(np.angle(X[0:hN]))
plt.subplot(3,1,3)
plt.plot(fs*np.arange(hN)/float(N),pX, 'g')

---
Parabola
p: center of the parabola
a: measure of concavity
b: offset

---
Peak interpolation
%beta
o
%gamma
o
%alpha
o
-1
+1
0
Center of the parabola:
hat{k}_p = hat{k} + {{%alpha - %gamma} over 2} (%alpha - 2%beta + %gamma)
hat{a} = %beta - {hat{k}_p over 4} (%alpha - %gamma)
Amplitude:

---
Peak interpolation
def peak_interp(mX, pX, ploc):
  # mX: magnitude spectrum, pX: phase spectrum,
  # ploc: locations of peaks
  # iploc, ipmag, ipphase: interpolated values
  val = mX[ploc]
  lval = mX[ploc-1]
  rval = mX[ploc+1]
  iploc = ploc + 0.5*(lval-rval)/(lval-2*val+rval)
  ipmag = val - 0.25*(lval-rval)*(iploc-ploc)
  ipphase = np.interp(iploc, np.arange(0, pX.size), pX)
  return iploc, ipmag, ipphase

---
Peak detection with interpolation

---
Sinusoidal synthesis

---
Sinusoid (sine wave)
Sinusoidal synthesis
alignl {y[n] = A_0[n] cos (2 %pi f_0[n]n+%phi_0)} newline newline alignl {A_0[n]: "instantaneous amplitude"} newline alignl {f_0[n]: "instantaneous frequency"} newline alignl {%phi_0: "initial phase"}
import matplotlib.pyplot as plt
import numpy as np
A = .8
F0 = 2.0
phi = np.pi/2
fs = 100
t = np.arange(-1, 1, 1.0/fs)
x = A * np.cos(2*np.pi*f0*t+phi)
plt.plot(t, x)

---
Spectral-based sinusoidal synthesis
F0 = 500.0
Fs = 10000.0
A0 = .8
phi0 = 1.5
Ns = 64
hNs = Ns/2
k = np.int(np.round(Ns*f0/fs))
mY[k] = A0 * Ns
pY[k] = phi0
Y[:hNs] = .5*mY*np.exp(1j*pY)
Y[hNs+1:]=Y[hNs-1:0:-1].conjugate()
plt.subplot(3,1,1)
plt.plot(mY, 'ro')
plt.subplot(3,1,2)
plt.plot(pY, 'bo')
y = np.real(ifft(Y))
yw[:hNs-1] = y[hNs+1:]
yw[hNs-1:] = y[:hNs+1]
plt.subplot(3,1,3)
plt.plot(yw, 'r')

---
Sinusoids in spectrum

---
Sinewave spectrum

---
Inverse of spectral sinusoid

---
Blackman-Harris main-lobe

---
Synthesis spectrum
iploc = 20.5, 130.3, 200.2
ipmag = -2.2, -4.3, -8.2
ipphase = 1.1, 3.2, 2.4

---
def genspecsines(iploc, ipmag, ipphase, N):
  Y = np.zeros(N, dtype = complex)
  hN = N/2
  for i in range(0, iploc.size):
    loc = iploc[i]
    if loc<1 or loc>hN-1: continue
    binremainder = round(loc)-loc;
    lb = np.arange(binremainder-4, binremainder+5)
    lmag = uf.genbh92lobe(lb) * 10**(ipmag[i]/20)
    b = np.arange(round(loc)-4, round(loc)+5)
    for m in range(0, 9):
      if b[m] < 0:
        Y[-b[m]]+=lmag[m]*np.exp(-1j*ipphase[i])
      elif b[m] > hN:
        Y[b[m]]+=lmag[m]*np.exp(-1j*ipphase[i])
      elif b[m]==0 or b[m]==hN:
        Y[b[m]]+=lmag[m]*np.exp(1j*ipphase[i])+lmag[m]*np.exp(-1j*ipphase[i])
      else:
        Y[b[m]]+=lmag[m]*np.exp(1j*ipphase[i])
    Y[hN+1:] = Y[hN-1:0:-1].conjugate()

---
Synthesis window

---
Synthesis window

---
Analysis / Synthesis
M = 801
window = hamming(M)
N = 1024
t = -40
freqs = 100.2, 200.3, 300.2
amps = .99, .7, .5
fs = 2000
Ns = 512

---
Implementation
w[n]
|X[k]|
Peak detection
Sine spectral
synthesis
x[n]
FFT
xw[n]
<X[k]
Y[k]
IFFT
yw[n]
Overlap-add
y[n]

---
def sine_model(x, fs, w, N, t):
  hN = N/2
  hM = (w.size+1)/2
  Ns = 512
  H = Ns/4
  hNs = Ns/2
  pin = max(hNs, hM)
  pend = x.size - max(hNs, hM)
  w = w / sum(w)
  ow = triang(2*H);
  sw[hNs-H:hNs+H] = ow
  bh = blackmanharris(Ns)
  bh = bh / sum(bh)
  sw[hNs-H:hNs+H] = sw[hNs-H:hNs+H] / bh[hNs-H:hNs+H]
  while pin<pend:
    xw = x[pin-hM:pin+hM-1] * w fftbuffer[:hM] = xw[hM-1:]
    fftbuffer[N-hM+1:] = xw[:hM-1]
    X = fft(fftbuffer)
    mX = 20 * np.log10( abs(X[:hN]) )
    ploc = peak_detection(mX, hN, t)
    pmag = mX[ploc]
    pX = np.unwrap( np.angle(X[:hN]) )
    iploc, ipmag, ipphase = peak_interp(mX, pX, ploc)
    plocs = iploc*Ns/N;
    Y = genspecsines(plocs, ipmag, ipphase, Ns)
    fftbuffer = np.real( ifft(Y) )
    yw[:hNs-1] = fftbuffer[hNs+1:]
    yw[hNs-1:] = fftbuffer[:hNs+1]
    y[pin-hNs:pin+hNs] += sw*yw
    pin += H
  return y

---
References
https://ccrma.stanford.edu/~jos/sasp/Spectrum_Analysis_Sinusoids.html

---
Credits
All the slides of this presentation are released under an Attribution-Noncommercial-Share Alike license.