Some basic mathematics
Sinusoidal model
(1 of 2)
Xavier Serra
Universitat Pompeu Fabra, Barcelona

---
Index
- Sinusoidal model
- Sinewaves in a spectrum
- Sinewaves as spectral peaks
- Time-varying sinewaves in spectrogram

---
Sinusoidal model
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n)} newline newline alignl {R: "number of sinewaves"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency (Hz)"} newline

---
Spectrum of sinewave
alignl{x[n] = A cos(2%pi k_0 n/N + %phi)} newline alignl{X[k]= A sum from{n=0} to{N-1} w[n] 1 over 2 {(e^{j 2%pi k_0 n/N} + e^{-j 2%pi k_0 n/N})} e^{-j 2%pi kn/N}}newline alignl{~~~~~ = A over 2 sum from{n=0} to{N-1} w[n] e^{j 2%pi k_0 n/N} e^{-j 2%pi kn/N} + A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi k_0 n/N} e^{-j 2%pi kn/N}}newline alignl{~~~~~ = A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi ( - k_0 + k)n/N} + A over 2 sum from{n=0} to{N-1} w[n] e^{-j 2%pi (k_0 + k)n/N}}newline alignl{~~~~~ = A over 2 W[k-k_0] + A over 2 W[k+k_0]}

---
Sinewaves as spectral peaks
- Sinusoid peak in spectrum
- Frequency resolution = 1/2 bin
- Improvement of frequency resolution by:
  - zero-padding
  - spectral interpolation

---
Spectral peaks and window-size
{alignl {size 24{"If" B_f = B_s f_s / M ~ ~ "and" %iDELTA = lline f_{k+1} - f_k rline}}}
{alignl {size 20 {B_s="main-lobe bandwidth of window"}}}newline {alignl {size 20 {f_s="sampling rate in Hz"}}}newline {alignl {size 20 {M="window size"}}}newline {alignl {size 20 {f_k "and" f_{k+1}="frequency of sinusoids in Hz"}}}
{alignl{size 24 {M geslant B_s f_s over %iDELTA = B_s {alignc f_s} over {lline f_{k+1} - f_k rline}}}}
{alignl {size 20{"If" f_0 = %iDELTA, ~"then"~ B_f leslant f_0}}} newline {alignl {size 20{"and"~ M geslant B_s f_s / f_0, ~"or"~ M geslant B_s P,}}} newline {alignl {size 20 {"where"~ P = "period in samples"}}}

---
{alignl {size 20{"Hamming window": B_s = 4}}} newline {alignl {size 20{f_s = 44100 "Hz"}}}newline {alignl {size 20{f_k = 440 "Hz"; f_{k+1} = 490 "Hz"}}}newline
{alignl{size 24 {M geslant B_s {alignc f_s} over {lline f_{k+1} - f_k rline} =4 {alignc 44100} over {lline 490 - 440 rline} = 3528}}}

---
Peak detection
alignl{size 20 {p_r = mX[k_0] ~"when"~ mX[k_0-1]<mX[k_0]>mX[k_0+1]}}newline alignl{size 18 {mX = "magnitude spectrum"; r = "peak number"; k_0 = "peak location"}}

---
Peak detection with zero-padding

---
Parabola
p: center of parabola
a: concavity measure
b: offset
{size 24 {alignl{x[n] = a (n - p)^2 + b}}}

---
Peak interpolation
%beta
o
%gamma
o
{alignl {size 24 {x[-1]~ = ~%ialpha~ = ~ mX[k_{%ibeta} -1]}}} newline {alignl {size 24 {x[0]~ = ~%ibeta~ = ~ mX[k_{%ibeta}]}}} newline {alignl {size 24 {x[1]~ = ~%igamma~ = ~ mX[k_{%ibeta} + 1]}}}
%alpha
o
-1
+1
0
Center of the parabola:
{hat k}_p = {hat k} + {{%alpha - %gamma} over 2} (%alpha - 2%beta + %gamma)
hat{a} = %beta - {hat k}_p over 4 (%alpha - %gamma)
Amplitude:

---
Peak detection with interpolation

---
Sinusoidal parameters from peaks
alignl{{hat k}_p} = lline X[k_p] rline + {0.5 * (lline X[k_p-1]rline -lline X[k_p+1]rline)}over {lline X[k_p-1]rline -2*lline X[k_p]rline + lline X[k_p+1] rline}newline newline newline alignl{f_p = f_s * {hat k}_p over {alignc N}}newline newline alignl{A_p = lline X[k_p]rline - 0.25 * (lline X[k_p - 1]rline - lline X[k_p+1]rline)*({hat k}_p - k_p)} newline newline alignl{ph_p = %angle X[{hat k}_p]} newline newline

---
Sinewaves in spectrogram
- Sinusoid stable peak track in spectrogram
- Stability identified by
  - frequency and amplitude in succesive frames
  - phase derivative in time/freq
alignl{"Condition for a peak" f_p "of frame" l "to be part of a track" t:}newline newline alignl{f_p[l] = f_t[l]~ "if"~ (lline f_p[l] -f_t[l-1] rline ~< ~threshold)}newline alignl{ ~~~~~~"and exists"~f_t[l-2], f_t[l-3],... ,f_t[l-L] }

---
References and credits
- More information on this topic from Wikipedia:
  - http://en.wikipedia.org/wiki/Additive_synthesis
  - http://en.wikipedia.org/wiki/Sinusoidal_model
- Good reference for Sinusoidal modeling by Julius O. Smith: https://ccrma.stanford.edu/~jos/sasp/Spectrum_Analysis_Sinusoids.html
- Sounds used taken from Freesound: http://www.freesound.org/people/xserra/packs/13038/
- All slides and code produced for this course are released using the CC Attribution-Noncommercial-Share Alike license or the Affero GPL license and available from https://github.com/MTG/sms-tools

---
Sinusoidal model
(1 of 2)
Xavier Serra
Universitat Pompeu Fabra, Barcelona