The Discrete Fourier Transform
Fundamental frequency detection
Xavier Serra
Universitat Pompeu Fabra, Barcelona

---
Index
- F0 detection in time domain
  - monophonic signals
- F0 detection in frequency domain
  - monophonic and polyphonic signals

---
F0 detection in time domain
Autocorrelation (with tapering)
alignl{Z^{'}_{xx}[k] = sum from {n=0} to {n=N-1-k} x[n] x[n+k]~~~k=-N+1,...,N-1}newline newline alignl{"where" ~k = "lag"} newline

---
YIN Algorithm ( Cheveigné and Kawahara, 2002)

---
F0 detection in frequency domain

---
Fundamental frequency detection
F0 detection
The fundamental frequency can be defined as the common divisor of the harmonic series that best explains the spectral peaks.

---
Two-way mismatch algorithm
(Maher and Beauchamp, 1994)
7F
alignl{"Err"_{p toward m} = sum from {n=1} to N E_%omega (%DELTA f_n, f_n ,a_n, A_"max")}newline alignl{~~~~~~~= sum from {n=1} to N %DELTA f_n cdot (f_n)^{-p}}newline alignl{~~~~~~~~~~+({a_n} over {A_"max"}) times [ q%DELTA f_n cdot (f_n)^{-p} - r]} newline newline alignl{%DELTA f_n:"diff. between a predicted and"}newline alignl{~~~~~~"its closest measured peaks"}newline alignl{f_n, a_n: "frequency and magnitude of"}newline alignl{~~~~~~~"predicted peaks"}newline alignl{A_"max": "maximum peak magnitude"}newline
6F
5F
4F
3F
2F
F
m
p

---
alignl{"Err"_{m toward p} = sum from {k=1} to K E_%omega (%DELTA f_k, f_k ,a_k, A_"max")}newline alignl{~~~~~~~= sum from {k=1} to K %DELTA f_k cdot (f_k)^{-p}+({a_k} over {A_"max"}) times [ q%DELTA f_k cdot (f_k)^{-p} - r]} newline newline alignl{%DELTA f_n:"diff. between a predicted and its closest measured peaks"}newline alignl{f_n, a_n: "frequency and magnitude of predicted peaks"}newline alignl{A_"max": "maximum peak magnitude"}newline
Total error:
alignl{"Err"_"total" = "Err"_{p toward m}/N ~+ ~ %rho "Err"_{m toward p}/K}newline
Maher and Beauchamp propose:

---
	Errp->m	Errm->p	Errtotal
50Hz	122.58	-3.0	7.49
100Hz	32.0	-3.0	3.83
200Hz	10.0	30.66	4.2
TWM error calculation from the frequencies: 200, 300, 500, 600, 700, 800.

---
F0 in polyphonic signals

---
Prominent pitch in polyphonic signals
(Salamon and Gómez, 2012)

---
References and credits
- More information on this topic from Wikipedia:
  - http://en.wikipedia.org/wiki/Fundamental_frequency
  - http://en.wikipedia.org/wiki/Pitch_detection_algorithm
  - http://en.wikipedia.org/wiki/Autocorrelation
- F0 detection algorithms:
  - A. de Cheveigné and H. Kawahara. “YIN, a fundamental frequency estimator for speech and music,” J. Acoust. Soc. Am. 111, 1917 (2002).
  - R. C. Maher and J. W. Beauchamp, “Fundamental frequency estimation of musical signals using a Two-Way Mismatch procedure,” J. Acoust. Soc. Am., vol. 95., no. 4, pp. 2254-2263 (1994).
  - J. Salamon and E. Gómez, "Melody extraction from polyphonic music signals using pitch contour characteristics," IEEE Transactions on Audio, Speech, and Language Processing, vol. 20, no. 6, pp. 1759–1770 (2012).
- Sounds used taken from Freesound: http://www.freesound.org/people/xserra/packs/13038/
- All slides and code produced for this course are released using the CC Attribution-Noncommercial-Share Alike license or the Affero GPL license and available from https://github.com/MTG/sms-tools