The Discrete Fourier Transform
Stochastic Model
Xavier Serra
Universitat Pompeu Fabra, Barcelona

---
Index
- Stochastic signals
- Stochastic model
- Stochastic approximation of sounds
- Stochastic model system

---
Residual modeling
Stochastic signals
- Stochastic processes
  - described by the laws of probability, mean, variance, probability distributions
- Autocorrelation
- Power spectral density
alignl{Z_{xx}[k] = sum from {n=0} to {n=N-1} x[n] x[n+k]~~~k=-N+1,...,N-1}
alignl{Xp [k] = lim csub {N rightarrow infinity} {abs{X[k]}}^2} newline alignl{"where "X[k] = sum from{n=0} to{N-1} {x[n] e^{-j 2%pi kn/N}}~~k=0,..., N-1} newline

---
Stochastic model
alignl{yst[n] = sum from {k=0} to {N-1} u[n] h[n-k]} newline newline alignl{u[n]: "white noise"}newline alignl{h[n]: "impulse response of filter approximating input signal" x[n]}newline
Spectral view:
alignl{Yst_l[k] = {lline {H}_l[k] rline} {lline {U}[k] rline} e^{j({%angle H[k]}+{%angle U[k]})} = {lline {tilde X}_l[k] rline} e^{j{%angle U[k]}} } newline newline alignl{{lline{tilde X}[k] rline}: "approximation of magnitude spectrum of input signal" x[n]}newline alignl{%angle U[k]: "spectral phases of noise signal"}newline alignl{l: "frame number"}newline

---
IIR-filter approximation
Filter approximation
y[n] = sum from {k=1} to K a_k x[n-k] + A u[n]
LPC model:
{hat x}[n] = - sum from {k=1} to K a_k x[n-k]
e[n] =x[n] - {hat x}[n] = x[n] + sum from {k=1} to K a_k x[n-k]
E = sum from {n= - infinity} to {infinity} e[n]^2 = sum from {n= - infinity} to {infinity} (x[n] + sum from {k=1} to K a_k x[n-k])^2
The error is minimized by minimizing the mean of the total squared error with
respect to each of the parameters.

---
Noise synthesis using IFFT
Envelope approximation
alignl{tilde a [k] = IDFT(LP(DFT(a[k]))) } newline alignl{LP: "low-pass filter"}
alignl{b [k] = IDFT(ZP(DFT(tilde a[k]))) } newline alignl{ZP: "zero-padding"}

---
Residual synthesis
Stochastic synthesis using LPC
{alignl {yst[n] = sum from {k=1} to K a_k u[n-k]}}newline {alignl {a_k: "filter coefficients"; u[n]: "white noise"}}newline
direct form
structure
lattice
structure

---
Stochastic synthesis using envelopes
alignl{yst[n] = IDFT({lline {tilde X}[k] rline} e^{j %angle U[k]})} newline

---
STFT implementation diagram
Stochastic model system
w[n]
|Yst[k]|
|X[k]|
x[n]
yst[n]
yw[n]
xw[n]
Overlap-add
Stochastic spec. synthesis
Stochastic approx.
X
IFFT
FFT
Random phase generation
<Yst[k]

---
References and credits
- More information on this topic from Wikipedia:
  - http://en.wikipedia.org/wiki/Stochastic_process
  - http://en.wikipedia.org/wiki/Linear_predictive_coding
- Sounds used taken from Freesound: http://www.freesound.org/people/xserra/packs/13038/
- All slides and code produced for this course are released using the CC Attribution-Noncommercial-Share Alike license or the Affero GPL license and available from https://github.com/MTG/sms-tools

---
Stochastic Model
Xavier Serra
Universitat Pompeu Fabra, Barcelona