The Discrete Fourier Transform
Sinusoidal plus Residual Model
Xavier Serra
Universitat Pompeu Fabra, Barcelona

---
Index
- Sinusoidal plus residual model
- Sinusoidal subtraction
- Sinusoidal plus stochastic model
- Harmonic plus residual or stochastic model
- Harmonic plus stochastic system

---
Sinusoidal plus residual model
Sinusoidal plus residual model
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n) +xr[n] = ys[n] + xr[n]} newline newline alignl {R: "number of sinusoidal components"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency (Hz)"} newline alignl {xr[n]= x[n] - ys[n]: "residual component"} newline alignl {ys[n]: "sinusoidal component"} newline

---
Spectral view
alignl {Y_l[k] = sum from {r=1} to {R_l} A_{(r,l)} W[k-{hat f}_{(r,l)}] + Xr_l[k] = Ys_l[k] + Xr_l[k] } newline newline alignl {W[k]: "spectrum of analysis window"} newline alignl {R_l: "number of sinusoidal components"} newline alignl {A_{(r,l)}: "amplitude of sinusoid"} newline alignl {{hat f}_{(r,l)}: "normalized frequency of sinusoid"} newline alignl {Xr_l[k] = X_l[k] - Ys_l[k]: "residual component spectrum"} newline alignl {Ys_l[k]: "sinusoidal component spectrum"} newline alignl {l: "frame number"} newline

---
Plot of sines + res

---
Sinusoidal plus stochastic model
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n) + yst[n] = ys[n] + yst[n]} newline alignl {R: "number of sinusoidal components"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency (Hz)"} newline alignl {yst[n]: "stochastic component"} newline alignl {ys[n]: "sinusoidal component"} newline
where:
alignl{yst_l[n] = sum from {k=0} to {N-1} u[n] h_l[n-k]} newline alignl{u[n]: "white noise"}newline alignl{h[n]: "impulse response of residual approximation"}newline alignl{l: "frame number"}newline

---
Spectral view
alignl {Y_l[k] = sum from {r=1} to {R_l} A_{(r,l)} W[k-{hat f}_{(r,l)}] + Yst_l[k] } newline alignl {W[k]: "spectrum of analysis window"} newline alignl {R_l: "number of sinusoidal components"} newline alignl {A_{(r,l)}: "amplitude of sinusoid"} newline alignl {{hat f}_{(r,l)}: "normalized frequency of sinusoid"} newline alignl {l: "frame number"} newline
where:
alignl{Yst_l[k] = {lline {tilde Xr}_l[k] rline} e^{j{%angle U[k]}} } newline alignl{{lline {tilde Xr}_l[k] rline}: "magnitude spectrum approximation of residual"}newline alignl{%angle U[k]: "spectral phases of noise"}newline alignl{l: "frame number"}newline

---
Implementation: Harmonic Model
Implementation: HpS model
wh[n]
|X[k]|
x[n]
pr
fr
Ar
F0
detection
Peak detection
FFT
X
xwh[n]
<X[k]
ph
f0
fh
Ah
Sine spectral
synthesis
wr[n]
-
X[k]
Yh[k]
FFT
X
+
Yr[k]
xwr[n]
Stochastic approximation
|Ys[k]|
<Ys[k]
Ys[k]
Random phase generation
Stochastic spec. synthesis
+
Y[k]
IFFT
yw[n]
Overlap-add
y[n]

---
References and credits
- https://ccrma.stanford.edu/~jos/sasp/Spectrum_Analysis_Sinusoids.html
- All slides and code produced for this course are released using the CC Attribution-Noncommercial-Share Alike license or the Affero GPL license and available from https://github.com/MTG/sms-tools