The Discrete Fourier Transform
Harmonic Modeling
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
http://mtg.upf.edu

---
Index
- Harmonic Model
- Sinusoids-Partials-Harmonics
- F0 detection
- Harmonic tracking
- Implementation

---
Harmonic model
alignl {yh[n] = sum from {k=1} to K A_k[n] cos (2 %pi kf_0[n]n)} newline newline alignl {K: "number of harmonic components"} newline alignl {A_k[n]: "instantaneous amplitude"} newline alignl {f_0[n]: "fundamental frequency"} newline

---
Sinusoids-Partials-Harmonics
- Any time-varying spectrum can be modeled as the sum of time-varying sinusoids.
- Most of the spectral bins in a spectrum do not correspond to actual partials of the analyzed sound.
- A sound partial is the result of a main mode of vibration of the generating system.
- Partials can be modeled as slowly time-varying sinusoids.
- A partial in the frequency domain can be identified by its spectral shape (magnitude and phase), its relation to other partials, and its time evolution.
- When the partials of a sound are related harmonically we call them harmonics.

---
F0 detection in time domain
Autocorrelation
alignl{Z_{xx}[k] = sum from {n=0} to {n=N-1} x[n] x[n+k]~~~k=-N+1,...,N-1}

---
(fs, x) = read('oboe.wav')
M = 400
str = .8*fs
xp = x[str:str+M]/float(max(x[str:str+M]))
z = np.correlate(xp,xp,'full')
plt.subplot(211)
plt.plot(np.arange(M)/float(fs), xp)
plt.subplot(212)
plt.plot(z[M-1:]/max(z),'r')

---
Fundamental frequency detection
F0 detection from spectral peaks
The fundamental frequency can be defined as the common divisor of the harmonic series that best explains the spectral peaks.
Steps:
Choose possible fundamental candidates.
Measure the “goodness” of the resulting harmonic series
compared with the spectral peaks.
Get the best candidate.

---
Two-way mismatch
error calculation
(Maher and Beauchamp, 94)
7F
6F
5F
4F
3F
2F
F

---
Total error:
Maher and Beauchamp propose:

---
TWM calculation from a harmonic series that includes the frequencies: 200, 300, 500, 600, 700, 800.

---
  p = 0.5
  q = 1.4
  r = 0.5
  rho = 0.33
  Amax = max(pmag)
  harmonic = np.matrix(f0cand)
  MaxNPM = min(maxnpeaks, pfreq.size)
  for i in range(0, MaxNPM) :
    difmatrixPM = harmonic.T * np.ones(pfreq.size)
    difmatrixPM = abs(difmatrixPM - np.ones((harmonic.size, 1))*pfreq)
    FreqDistance = np.amin(difmatrixPM, axis=1)
    peakloc = np.argmin(difmatrixPM, axis=1)
    Ponddif = np.array(FreqDistance) * (np.array(harmonic.T)**(-p))
    PeakMag = pmag[peakloc]
    MagFactor = 10**((PeakMag-Amax)/20)
    ErrorPM = ErrorPM + (Ponddif + MagFactor*(q*Ponddif-r)).T
    harmonic = harmonic+f0cand
  MaxNMP = min(maxnpeaks, pfreq.size)
  for i in range(0, f0cand.size) :
    nharm = np.round(pfreq[:MaxNMP]/f0cand[i])
    nharm = (nharm>=1)*nharm + (nharm<1)
    FreqDistance = abs(pfreq[:MaxNMP] - nharm*f0cand[i])
    Ponddif = FreqDistance * (pfreq[:MaxNMP]**(-p))
    PeakMag = pmag[:MaxNMP]
    MagFactor = 10**((PeakMag-Amax)/20)
    ErrorMP[i] = sum(MagFactor * (Ponddif + MagFactor*(q*Ponddif-r)))
  Error = (ErrorPM/MaxNPM) + (rho*ErrorMP/MaxNMP)
  f0index = np.argmin(Error)
  f0 = f0cand[f0index]

---
Peak continuation
Peak continuation
McAulay and Quatieri approach:
frequency tracker
frequency tracks of speech

---
Harmonic tracking
f0 = fd.f0DetectionTwm(iploc, ipmag, N, fs, f0et, minf0, maxf0)
hf = (f0>0)*(f0*np.arange(1, nH+1))
hi = 0
npeaks = ploc.size
while f0>0 and hi<nH and hf[hi]<fs/2 :
   dev = min(abs(iploc/N*fs - hf[hi]))
   pei = np.argmin(abs(iploc/N*fs - hf[hi]))
   if (hi==0 or not any(hloc[:hi]==iploc[pei])) and dev<maxhd*hf[hi]:
      hloc[hi] = iploc[pei]
      hmag[hi] = ipmag[pei]
      hphase[hi] = ipphase[pei]
    hi += 1
hloc = (hloc!=0) * (hloc*Ns/N)

---
frequency trajectories
magnitude trajectories

---
Implementation: Harmonic Model
Implementation: Harmonic model
w[n]
|X[k]|
F0
detection
Peak detection
pr
x[n]
fr
Ar
FFT
xw[n]
<X[k]
ph
f0
fh
Ah
Analysis
Synthesis
Sine spectral
synthesis
Yh[k]
IFFT
yhw[n]
Overlap-add
yh[n]

---
def harmonicModel(x, fs, w, N, t, nH, minf0, maxf0, f0et, maxhd):
Ns = 512
w = w / sum(w)
ow = triang(2*H)
sw[hNs-H:hNs+H] = ow
bh = blackmanharris(Ns) / sum(bh)
sw[hNs-H:hNs+H] = sw[hNs-H:hNs+H] / bh[hNs-H:hNs+H]
while pin<pend:
#-----analysis-----
  xw = x[pin-hM1:pin+hM2] * w
  fftbuffer[:hM1] = xw[hM2:]
  fftbuffer[N-hM2:] = xw[:hM2]
  X = fft(fftbuffer)
  mX = 20 * np.log10( abs(X[:hN]) )
  ploc = PP.peakDetection(mX, hN, t)
  pX = np.unwrap( np.angle(X[:hN]) )
  iploc, ipmag, ipphase = PP.peakInterp(mX, pX, ploc)
  f0 = fd.f0DetectionTwm(iploc, ipmag, N, fs, f0et, minf0, maxf0)
  hf = (f0>0)*(f0*np.arange(1, nH+1))
  while f0>0 and hi<nH and hf[hi]<fs/2 :
    dev = min(abs(iploc/N*fs - hf[hi]))
    pei = np.argmin(abs(iploc/N*fs - hf[hi]))
    if ( hi==0 or not any(hloc[:hi]==iploc[pei]) ) and dev<maxhd*hf[hi] :
      hloc[hi] = iploc[pei]
      hmag[hi] = ipmag[pei]
      hphase[hi] = ipphase[pei]
    hi += 1
  hloc = (hloc!=0) * (hloc*Ns/N)
  #-----synthesis-----
  Yh = GS.genSpecSines(hloc, hmag, hphase, Ns)
  fftbuffer = np.real( ifft(Yh) )
  yh[:hNs-1] = fftbuffer[hNs+1:]
  yh[hNs-1:] = fftbuffer[:hNs+1]
  y[pin-hNs:pin+hNs] += sw*yh
  pin += H
return y

---
References
- http://en.wikipedia.org/wiki/Fundamental_frequency
- http://en.wikipedia.org/wiki/Pitch_detection_algorithm

---
Credits
All the slides of this presentation are released under an Attribution-Noncommercial-Share Alike license.