The Discrete Fourier Transform
[text for DFT-1.odp]

Welcome again to the Audio Signal Processing for Music Applications course!!

1.
This is the first lecture in which we really start the core topics of the course. We introduce the Discrete Fourier Transform. We will dedicate two lectures to this topics.

2.
In this first lecture on the DFT we will first present the DFT equation and then we will discuss the two basic components of this equation, the complex exponentials and the scalar product between the input signal and the complex exponentials.

3.
The Discrete Fourier Transform can be expressed by this equation

….

where n is discrete time index. We normalize the time, that is we use a sampling period T equal to 1.

k is discrete frequency index

the angular frequency omega sub k is 2 pi k divided by n

the frequency in Hz is equal to the sampling rate times k over N

this is a discrete representation of the Fourier transform that becomes much simpler to understand, no integrals, and computationally it becomes much more useful. So from now on, when we talk about the Fourier Transform, we basically refer to this equation.

4.
These are the plots of the input and output signals of the DFT as we normally like to see them.

the top plot is the input signal x, 512 samples of an oboe sound centered around 0, with the time expressed in samples.

the two bottom plots represent the output of the DTF, the spectrum of x, capital X

capital X is a complex function and we show it in polar form, thus showing the amplitude and phase of the numbers for the positive half of the 512 output samples.

The amplitude is shown in a decibel scale and the phase is shown unwrapped, without restricting it to the modulus 2 pi view.

With these plots we can see that the input signal is a periodic signal, it is the note A4 played by an oboe. In the magnitude spectrum we identify the harmonics of the sound, which are only prominent in the low frequencies. The phase spectrum is more dificult to interpret but we can see the phase at location 0 of time, of the harmonics of the sound.

5.
New lets decompose the DFT equation. First let's talk about the complex exponentials that are part of the equation.

Let's refer to these complex exponentials as s bar sub k. Using Euler's identity we can express the complex exponentials as ….

Let's compute the values of these functions for the particular case of N = 4

…...

6.
These are the plots of the set of complex sinewaves for a DFT of size N = 8

there are 8 sinewaves, k from 0 to 7, and 8 samples in each sinewave, n from 0 to 7

blue is the real part, thus the cosine

green is the imaginary part, thus the sine

the first sinewave is of frequency zero, k = 0, thus the real part, cosine is 1 and the imaginary part, sine is 0

k = 1 is one period in the 8 samples

we see the simetries

7.
After understanding the complex exponentials term of the DFT the other step is the scalar product, or inner product between the input signal x[n] and these complex exponentials.

The scalar product of two sequences, x and a complex exponential s sub k, is expressed by this equation.

This is the DFT of x

coefficient of projection

8.
These are the plots of the result of computing the scalar product of a sequence x with a series of 8 set of complex sinewaves, thus of computing the DFT of x

….

9.
Most of the references I used to prepare this lecture come from the website of Julius Smith on the Mathematics of the Discrete Fourier Transform.

---------------

This is all for this class. We have

Thanks for your attention!!