The Discrete Fourier Transform
Harmonic Modeling
(2 of 2)
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
http://mtg.upf.edu

---
Index
- Harmonic Model equation
- F0 detection: frequency domain
- Harmonic tracking
- System diagram

---
Harmonic model
alignl {yh[n] = sum from {k=1} to K A_k[n] cos (2 %pi kf_0[n]n)} newline newline alignl {K: "number of harmonic components"} newline alignl {A_k[n]: "instantaneous amplitude"} newline alignl {f_0[n]: "fundamental frequency"} newline

---
Fundamental frequency detection
F0 detection from spectral peaks
The fundamental frequency can be defined as the common divisor of the harmonic series that best explains the spectral peaks.
Steps:
Choose possible fundamental candidates.
Measure the “goodness” of the resulting harmonic series
compared with the spectral peaks.
Get the best candidate.

---
F0 candidates
Mmag = max(pmag_temp)
Mloc1 = np.argmax(pmag_temp)
pmag_temp[Mloc1] = -100
Mloc2 = np.argmax(pmag_temp)
pmag_temp[Mloc2] = -100
Mloc3 = np.argmax(pmag_temp)
pmag_temp[Mloc3] = -100
nCand = 6
f0c[:nCand] =
(pfreq[Mloc1]*np.ones(nCand))/(np.arange(nCand,0,-1))
f0c[nCand:nCand*2] =
(pfreq[Mloc2]*np.ones(nCand))/(np.arange(nCand,0,-1))
f0c[nCand*2:nCand*3] =
(pfreq[Mloc3]*np.ones(nCand))/(np.arange(nCand,0,-1))

---
Goodness measure of candidates
Two-way mismatch
error calculation
(Maher and Beauchamp, 94)
7F
6F
5F
4F
3F
2F
F

---
Total error:
Maher and Beauchamp propose:

---
TWM calculation from a harmonic series that includes the frequencies: 200, 300, 500, 600, 700, 800.

---
Harmonic tracking
f0 = fd.f0DetectionTwm(iploc, ipmag, N, fs, f0et, minf0, maxf0)
hf = (f0>0)*(f0*np.arange(1, nH+1))
hi = 0
npeaks = ploc.size
while f0>0 and hi<nH and hf[hi]<fs/2 :
   dev = min(abs(iploc/N*fs - hf[hi]))
   pei = np.argmin(abs(iploc/N*fs - hf[hi]))
   if (hi==0 or not any(hloc[:hi]==iploc[pei])) and dev<maxhd*hf[hi]:
      hloc[hi] = iploc[pei]
      hmag[hi] = ipmag[pei]
      hphase[hi] = ipphase[pei]
    hi += 1
hloc = (hloc!=0) * (hloc*Ns/N)

---
Implementation: Harmonic Model
Harmonic model: system diagram
w[n]
|X[k]|
F0
detection
Peak detection
pr
x[n]
fr
Ar
FFT
xw[n]
<X[k]
ph
f0
fh
Ah
Analysis
Synthesis
Sine spectral
synthesis
Yh[k]
IFFT
yhw[n]
Overlap-add
yh[n]

---
References
- http://en.wikipedia.org/wiki/Fundamental_frequency
- http://en.wikipedia.org/wiki/Pitch_detection_algorithm

---
Credits
All the slides of this presentation are released under an Attribution-Noncommercial-Share Alike license.