Fourier Theorems
Fourier Transform
properties
(2 of 2)
Xavier Serra
Universitat Pompeu Fabra, Barcelona
[Speaker Notes: In the previous lecture we started discussing some properties of the Discrete Fourier Transform. We continue in this one with some more properties that will be useful when using the DFT.]

---
Index
- Phase unwrapping
- Zero padding
- Power & amplitude in dB
- Fast Fourier Transform (FFT)
- FFT and zero-phase windowing
- Analysis/synthesis
[Speaker Notes: We will talk about ...]

---
Phase unwrapping
[Speaker Notes: Phase unwrapping is a way to represent the phase spectrum computed by the DFT in a way that is easier to visualize and understand. ...]

---
Zero-padding
[Speaker Notes: Zero-padding means to add zeros at the end of a signal. In the context of the DFT if we zero-pad in one domain it produces an interpolated signal in the other domain. ...]

---
Power
sum from{n=-N/2}to{N/2-1} {lline x(n) rline} ^{2} = {{1}over{N}} sum from{k=-N/2} to{N/2-1} {lline X(k) rline} ^{2}
sum from{n=N/2}to{N/2-1} {lline x(n) rline} ^{2} = 11.81182
{{1}over{N}} sum from{k=N/2} to{N/2-1} {lline X(k) rline} ^{2} = 11.81182
[Speaker Notes: This property relates with the energy, or power, that a signal has. The power computer in the time domain can also be computed in the frequency domain. ....]

---
Amplitude in Decibels
[Speaker Notes: When the obtain the polar representation of the spectrum of the signal the magnitude is obtained by computing the absolute value, a linear measure. However for the case of sounds, a more intuitive representation of the magnitude can be obtained by calculating the dB value. ....]

---
Fast Fourier Transform
Coley-Tukey algorithm: breaks down recursively the DFT of a power of 2 size into two pieces of size N/2.
[Speaker Notes: When we have to compute the DFT many times, which will be quite often, it is very convenient to use an efficient implementation of the equation. This is the FFT. ....]

---
[Speaker Notes: Here is a measure of the difference in computational cost between the direct implementation of the DFT equation versus the FFT implementation. ...]

---
FFT and zero-phase windowing
[Speaker Notes: This is the way that we will try to always compute the spectrum of a signal, what is call zero-phase windowing. ...]

---
Analysis/synthesis
|X[k]|
x[n]
y[n]
FFT
IFFT
<X[k]
[Speaker Notes: We saw that the DFT was an invertible operation; after computing the spectrum we can compute its inverse DFT and get back the original spectrum. This allows to perform analysis and synthesis operation of a sound. ...]

---
References and credits
- More information on this topic:
  - https://en.wikipedia.org/wiki/Discrete_Fourier_transform
  - https://en.wikipedia.org/wiki/Fast_Fourier_transform
- Sounds used taken from Freesound: http://www.freesound.org/people/xserra/packs/13038/
- Good reference for the DFT by Julius O. Smith: https://ccrma.stanford.edu/~jos/mdft/
- The slides and code are released using the CC Attribution-Non Commercial-Share Alike license or the Affero GPL license and available from https://github.com/MTG/sms-tools

---
Fourier Transform
properties
(2 of 2)
Xavier Serra
Universitat Pompeu Fabra, Barcelona
[Speaker Notes: We have gone through some more properties of the DFT. This are all the concepts that will show up when we use the DFT for processing real sounds. To fully understand them you should both study what I just presented and practice them with real signals. Make sure that you spend time with the labs that we propose. This is all for today, thanks for your attention!]