The Discrete Fourier Transform
Sinusoidal plus Residual Modeling
Xavier Serra
Music Technology Group
Universitat Pompeu Fabra, Barcelona
http://mtg.upf.edu

---
Index
- Sinusoidal plus residual model
- Sinusoidal subtraction
- Stochastic modeling
- Stochastic approximation of residual
- Implementation

---
Sinusoidal plus residual model
Sinusoidal plus Residual model
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n) + yr[n]} newline alignl {R: "number of sinusoidal components"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency"} newline alignl {yr[n]: "residual signal"} newline
when yr[n] is an stochastic signal, it can be modeled as filtered white noise:
alignl{yr_l[n] =ys_l[n] = sum from {k=0} to {N-1} u[n] h_l[n-k]} newline alignl{u[n]: "white noise"}newline alignl{h[n]: "impulse response of filter"}newline alignl{l: "frame number"}newline
alignl {yr[n] = x[n] - sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n)}
otherwise:

---
Spectral view of model
alignl {Y_l[k] = sum from {r=1} to {R_l} A_{(r,l)} W[k-{hat f}_{(r,l)}] + Yr_l[k]} newline alignl {W: "spectrum of analysis window"} newline alignl {R_l: "number of sinusoidal components"} newline alignl {A_{(r,l)}: "Amplitude of sinusoid"} newline alignl {{hat f}_{(r,l)}: "Normalized frequency of sinusoid"} newline alignl {Yr_l: "residual spectrum"} newline alignl {l: "frame number"} newline
when e[n] is an stochastic signal, it can be modeled as filtered white noise:
alignl{Yr_l[k] = Ys_l[k] = U[k]H_l[k]} newline alignl{U: "white noise spectrum"}newline alignl{H_l: "frequency response of filter"}newline
otherwise:
alignl {Yr_l[k] = X_l[k] - Y_l[k]}

---
xw = x[pin-hM1:pin+hM2] * w
fftbuffer[:hM1] = xw[hM2:]
fftbuffer[N-hM2:] = xw[:hM2]
X = fft(fftbuffer)
mX = 20 * np.log10(abs(X[:hN]))
ploc = PP.peakDetection(mX, hN, t)
pX = np.unwrap(np.angle(X[:hN]))
iploc, ipmag, ipphase = PP.peakInterp(mX, pX, ploc)
iploc = (iploc!=0) * (iploc*Ns/N)
ri = pin-hNs-1
xr = x[ri:ri+Ns]*wr
fftbuffer[:hNs] = xr[hNs:]
fftbuffer[hNs:] = xr[:hNs]
Xr = fft(fftbuffer)
Ys = GS.genSpecSines(iploc, ipmag, ipphase, Ns)
Yr = Xr-Ys;
fftbuffer = np.real(ifft(Ys))
ysw[:hNs-1] = fftbuffer[hNs+1:]
ysw[hNs-1:] = fftbuffer[:hNs+1]
fftbuffer = np.real(ifft(Yr))
yrw[:hNs-1] = fftbuffer[hNs+1:]
yrw[hNs-1:] = fftbuffer[:hNs+1]

---
Residual modeling
Stochastic signals
- Stochastic processes
  - described by the laws of probability, mean, variance, probability distributions
- Autocorrelation
- Power spectral density
alignl{Z_{xx}[k] = sum from {n=0} to {n=N-1} x[n] x[n+k]~~~k=-N+1,...,N-1}
alignl{Xp [k] = lim csub {N rightarrow infinity} {abs{X[k]}}^2} newline alignl{"where "X[k] = sum from{n=0} to{N-1} {x[n] e^{-j 2%pi kn/N}}~~k=0,..., N-1} newline

---
Stochastic modeling
alignl{ys[n] = sum from {k=0} to {N-1} u[n] h[n-k]} newline newline alignl{u[n]: "white noise"}newline alignl{h[n]: "impulse response of filter"}newline
Spectral view:
alignl{Ys_l[k] = {lline {tilde X}_l[k] rline} e^{%angle U[k]} } newline newline alignl{{lline{tilde X}[k] rline}: "approximation of magnitude spectrum of input signal"}newline alignl{%angle U[k]: "spectral phases of noise"}newline alignl{l: "frame number"}newline

---
def stochasticModel(x, w, N, H, stocf) :
  hN = N/2
  hM = (w.size)/2
  pin = hM
  pend = x.size-hM
  yw = np.zeros(w.size)
  y = np.zeros(x.size)
  w = w / sum(w)
  ws = hanning(w.size)*2
  while pin<pend:
    xw = x[pin-hM:pin+hM] * w
    X = fft(xw)
    mX = 20 * np.log10( abs(X[:hN]) )
    mXenv = resample(np.maximum(-200, mX), mX.size*stocf)
    mY = resample(mXenv, hN)
    pY = 2*np.pi*np.random.rand(hN)
    Y[:hN] = 10**(mY/20) * np.exp(1j*pY)
    Y[hN+1:] = 10**(mY[:0:-1]/20) * np.exp(-1j*pY[:0:-1])
    fftbuffer = np.real(ifft(Y))
    y[pin-hM:pin+hM] += H*ws*fftbuffer
    pin += H
  return y

---
Stochastic model of residual
Stochastic modeling of residual
alignl {y[n] = sum from {r=1} to R A_r[n] cos (2 %pi f_r[n]n) + ys[n]} newline alignl {R: "number of sinusoidal components"} newline alignl {A_r[n]: "instantaneous amplitude"} newline alignl {f_r[n]: "instantaneous frequency"} newline alignl {ys[n]: "stochastic signal"} newline
Spectral view:
alignl{Ys_l[k] = {lline {tilde Xr}_l[k] rline} e^{%angle U[k]} } newline newline alignl{{lline {tilde Xr}_l[k] rline}: "approximation of magnitude spectrum of input signal"}newline alignl{%angle U[k]: "spectral phases of noise"}newline alignl{l: "frame number"}newline

---
IIR-filter approximation
IIR model of residual
y[n] = sum from {k=1} to K a_k x[n-k] + A u[n]
LPC model:
{hat x}[n] = - sum from {k=1} to K a_k x[n-k]
e[n] =x[n] - {hat x}[n] = x[n] + sum from {k=1} to K a_k x[n-k]
E = sum from {n= - infinity} to {infinity} e[n]^2 = sum from {n= - infinity} to {infinity} (x[n] + sum from {k=1} to K a_k x[n-k])^2
The error is minimized by minimizing the mean of the total squared error with
respect to each of the parameters.

---
Residual synthesis
Residual synthesis
Noise generation:
  - Algorithms for random number generation
  - White noise, other types of noises
  - Gaussian noise
direct form
structure
lattice
structure

---
Noise synthesis using IFFT
Noise synthesis using IFFT

---
Implementation: Harmonic Model
Implementation: HpS model
wh[n]
|X[k]|
x[n]
pr
fr
Ar
F0
detection
Peak detection
FFT
X
xwh[n]
<X[k]
ph
f0
fh
Ah
Sine spectral
synthesis
wr[n]
-
Xr[k]
Yh[k]
FFT
X
+
Yr[k]
xwr[n]
Stochastic approximation
|Ys[k]|
<Ys[k]
Ys[k]
Random phase generation
Stochastic spec. synthesis
+
Y[k]
IFFT
yw[n]
Overlap-add
y[n]

---
References
- https://ccrma.stanford.edu/~jos/sasp/Spectrum_Analysis_Sinusoids.html
- http://en.wikipedia.org/wiki/Stochastic_process
- http://en.wikipedia.org/wiki/Linear_predictive_coding
- Sounds: http://www.freesound.org/people/xserra/packs/13038/

---
Credits
All the slides of this presentation are released under an Attribution-Noncommercial-Share Alike license.